Rev – 08-01-05; 12-05; 07-07; 06-09; *02-10-11                                                                             S.A.C #

APPLICATION FOR ARMS APPROVAL

NORTH-SOUTH SKIRMISH ASSOCIATION

NAME: _________________________	DATE OF REVIEW______________
ADDRESS:______________________	N-SSA ID NUMBER_____________
CITY:__________________________	UNIT#_________ REGION________
STATE:_________________________	SINGLE____ PRODUCTION______
ZIP CODE_______________________	DATE CARD ISSUED____________
TYPE OF ARM: Smoothbore, Front Sight Only

MODEL:  C.S. Macon Altered M-1842, Type 3 (Battlefield Salvaged)

| Taken from original C.S. arms App’d for use in N-SSA matches, by Board action, 08-05 | O R I G | R E P R | I R O N | B R A S | Dimensions | Original | Repro | Tol+/- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Overall Length | 52.0 |  | 1.0” |
| Barrel – Made by – Breech - Made by – Bayonet Stud - bottom of bbl at 34.625” |  |  |  |  | Barrel Length | 36.0 |  | .5 |
| Lock – M-1842 |  |  |  |  | Rear Sight Loc | N/A |  | .375 |
| Stock - M-1842 |  |  |  |  | *Front Sight Loc | 32.750 |  | * .5 |
| Trigger Guard Assembly - M-1842 |  |  |  |  | Overall Stock Length | 49.0 |  | .5 |
| Patch Box – N/A |  |  |  |  | *Front Band | 30.25 |  | * .5 |
| Butt Plate - M-1842 |  |  |  |  | Middle Band | 24.5 |  | .375 |
| Bands – M-1842, Front band held in place w/ band spring |  |  |  |  | Bottom Band | 10.625 |  | .375 |
| Nose Cap – N/A |  |  |  |  | Drop in stock | 2.5 |  | .5 |
| Rear Sight – N/A |  |  |  |  | Trig to Butt Plate | 13.5 |  | .5 |
| Front Sight – Standard M-1842 blade on forward strap of Front Band, 0.125” high |  |  |  |  | Sling Swivel | Bow/Mid Band |  | .375 |
|  |  |  |  |  | Caliber | .69 |  | .010 |
|  |  |  |  |  | Number of Grooves | 0 |  |  |

*N.B. – The +/- tol. for FSL & FB must be the same as the OASL due to the front band being even with the stock tip, & the Front Sight being mounted on the Front Band

COMMITTEE USE ONLY:	         BOARD ACTION:
APPROVED_____ DISAPPROVED_____	         APPROVED___ DISAPPROVED_____
Remarks if any on back top of form	         LETTER SENT____________________
	         LETTER ATTACHED______________
AUTHORIZED SIGNATURE:____________________	         COPY TO EXEC SECTRY__________
	         COPY TO ADJ____________________

INSPECTOR’S COMP.  # _____________